## Slide 1: Flow Cytometry Workshop: Principles and Methods
IOCB Prague, October 7, 2017
Presented by:
Scientists from IOCB
Experts from BD Biosciences
Sponsored by:
Biochemical Phramacology │ Flow Cytometry Lab

## Slide 2: Program:
9:00 - 9:10 Registration
9:10 - 9:20 Welcome Introduction
9:20 - 10:30 Basics of Flow Cytometry
11:00 - 12:00 Fluorophores and Compensations: Fundamental Principles
Trends in Fluorescent dyes
13:00 – 14:30 Experiment planning (Panel- and experiment design including controls)
Applications – part I
15:00 – 16:30 Applications – part II
Times Sessions
10:30 – 11:00 Coffee break
12:00 – 13:00 Lunch
14:30 – 15:00 Coffee break

## Slide 3: Biochemical Pharmacology: Flow Cytometry Laboratory
Services
The Flow Cytometry Laboratory provides the art of instrumentation and resources for fluorescent analysis of cells at the single cell level (BD LSR Fortessa), including high-speed fluorescence activated cell sorting (BD FACSAria IIu).
Our goal is to provide expertise in flow cytometry areas of experimental design, instrument knowledge and training, data analysis and cell sorting.

## Slide 4: Biochemical Pharmacology: Flow Cytometry Laboratory
Jana Gϋnterová
Flow Cytometry Operator
BD LSR Fortessa
jana.gunterova@uochb.cas.cz
Alena Keprová
Training new users, Consultancy
Flow Cytometry Operator
BD, LSR Fortessa, BD FACS AriaII
alena.keprova@uochb.cas.cz
Any questions? Email us at cytometry@uochb.cas.cz
Miroslav Hájek
Experiment design, Consultancy
Miroslav.hajek@uochb.cas.cz
People

## Slide 5: Instruments
Analyzer:
BD LSRFortessa:
5 lasers: UV (355 nm), violet (405 nm), blue (488 nm), yellow-green (561 nm), red (633 nm)
20 detector analyzer capable of measuring 18 colors simultaneously
High throughput 96-well autosampler (HTS)
Acquisition workstation – PC with BD FACS Diva 8.0
Location: C 1.32

## Slide 7: Instruments
Cell sorter (FACS)
BD FACSAria II:
3 lasers: violet (405 nm), blue (488 nm), red (633 nm)
11 detector analyzer capable of measuring 9 colors simultaneously
Cells can be brought in: 15 ml Falcon, 5 ml FACS tubes, 1.5 ml Eppendorfs
Collection device: falcons (2-way sort), tubes and Eppendorfs (4-way sort), slides, well-plates
Temperature control, nozzles: 70, 85 and 100 µm
Location: A 2.29

## Slide 9: Biochemical Pharmacology │ Flow Cytometry Laboratory
Basic principles of Flow Cytometry
Topics Covered:
What is Flow Cytometry?
History of Flow Cytometry
Which particles can be analyzed?
What is measured? (FSC, SSC? Relative intensity of fluorescence)
Instrumentation: Fluidic system
Optical system
Electronic system
Data visualization, Plots and gating strategies

## Slide 10: Basic principles of Flow Cytometry
Definition:
analysis of the physical properties of single cells or other biological particles
single particle passes through a flow cell → particle is iluminated by laser source → → detection and analysis of scattered / emitted light
This information can be used to individually sort or separate subpopulations of cells.
Measurable parameters:
Relative size (FSC)
Relative internal complexity (SSC)
Relative fluorescence intensity (FL)

## Slide 11: Basic principles of Flow Cytometry
Historical Perspective: Evolution of Flow Cytometry
17th Century
1879
1934
1947 to 1949
1953
1965
1968
1970s onwards
Development of light microscope by Leeuwenhoek
Principles of Droplet formation by Lord Rayleigh
Counting of RBCs by Moldavan by forcing a suspension of cells through capillary tube.
The first apparatus for detecting bacteria in a LAMINAR SHEATH steam of air
Optical counting of RBCs by Crosland-Taylor by use of laminar flow principles
Application of Sweet's principle and Coulter principle to develop the first cell sorter by M. Fulwyler
Development of electrostatic inject droplet deflection by Richard Sweet
Development of fluorescence based cell sorter by Wolfgang Gohde
Development of FACS and other advances

## Slide 12: Basic principles of Flow Cytometry
Cells
Chromosomes
Bacteria
Yeast
Microparticles (beads)
Microvesicles Nanopartcles?
What type of particles can be analyzed in cytometer?

## Slide 13: Basic principles of Flow Cytometry
What particle sizes can be analyzed?

## Slide 14: Instrument overview
Where are samples run?
Flow cytometry integrates fluidic, optics, and electronics.

## Slide 15: Instrumentation
What is sheat fluid?
Sheath flow is the solution that runs in a flow cytometer
Depending on experimental needs, different formulations of sheath fluid can be used
The purpose of FLUIDICS SYSTEM is to transport sample to laser intercept!
"After the intercept, the cells either flow into the waste or, in the case of a cell sorter, the stream is broken into droplets, and the appropriate droplet is charged and sorted."
1. Fluidic System

## Slide 16: Fluidic System
The sample is introduced into the running sheath fluid in the FLOW CELL
Sample is hydrodynamically focused in the core stream
Sheath fluid and sample do not mix
Diameter of Flow Cell determines size of largest particle to pass (smallest part in analyzers)
Reduction of cross-section causes laminar fluidics
Sample flow rate adjustable

## Slide 17: Instrumentation
What happens when we increase the flow rate? And what are the consequences of this?
The pressure of the sheath remains the same.
Pressure of sample line will increase.
Core stream of cells will become wider.
Not optimally aligned with the laser at high flow rates!
It is better to have concentrated samples at low flow rate than diluted sample at high flow rate (higher precision)

## Slide 18: Instrumentation
2. Optical System
Optics System allows the excitation and emission of the emitted light
(components involved in fluorescent detection)
Laser excitation optics x collection optics

## Slide 19: Laser as excitation source!
Different lasers are used to optimally excite fluorochromes.
This guarantees that the potential of the fluorochrome is optimally exploited.
BUV395
BV421
FITC
PE-Cy7
APC
Optical System

## Slide 20: But how does the flow cytometer know that it is the same cell passing the different laser?
Laser delay time
The stream is a constant flow with a constant velocity.
This allows to estimate the laser delay time:
  How long does it take to reach the second, third and fourth laser from the first laser?
Based on the laser delay the software will combine the measured signals to one event (cell)

## Slide 21
Generation of light scatter

## Slide 22: Optical System
Forward scatter channel
the relative size (FSC)
Forward scatter detector
Coherent light source (488 nm)
Forward scatter channel:
detect the amount of light scattered in the forward direction
(along the same axis that the laser light is traveling)
particle passes through the focus
→ scattered light is detected by a photodetector
→ an electrical pulse is generated presented to the signal processing electronics

## Slide 23: Optical System
Forward scatter detector
The forward scatter obscuration bar interacts with laser light
Many cytometers use optical fibers to direct collected light to the fluorescence and side scatter detection system. In these types of systems, the output of the collection lens is focused on the ends of fibers, which are routed to the detection path. This can be very advantageous in overall cytometer design.

## Slide 24: Optical System
Intensity of forward scatter:
is most influenced by size of particle

## Slide 25: Optical System
Forward scatter channel
the relative size (FSC)
Forward scatter detector
Coherent light source (488 nm)
Forward scatter channel:
detect the amount of light scattered in the forward direction
(along the same axis that the laser light is traveling)
particle passes through the focus
→ scattered light is detected by a photodetector
→ an electrical pulse is generated presented to the signal processing electronics

## Slide 26: Optical System
Side scatter channel (SSC):
detect the amount of light scattered to the side
(90° to the axis that the laser light is traveling)
intensity of SSC is most influenced by the shape and optical homogeneity of cells

## Slide 27: Optical System
Using a fluorescence in Flow Cytometry
or cells
transfected with fluorescent proteins
What is Fluorescence light?
The fluorochrome absobs energy from the laser and releases the absorbed energy by:
Vibration and heat dissipation
b) Emission of photons of a longer wavelength =====> FLUORESCENCE
Stokes shift: energy difference between the wavelength of absorption and emission

## Slide 28: Optical System
Fluorescence detection:
Fluorescence emitted by each fluorochrome is usually detected in a unique fluorescence channel.
Specificity controlled by the wavelength selectivity of optical filters and mirrors.
Fluorescence detector
(PMT3, PMT4 etc.)
SSC detector photo multiplier tube (PMT)
FCS detector photo diode
(signal levels are high)

## Slide 29: From Fluorescence to Computer Display
Each cell generates a quanta of fluorescence.
Individual cell fluorescence quanta is picked up by the various detectors PMT ' s (photomultiplier tubes).
PMT's convert light into electrical signals (pulses).
These electrical signals are amplified and digitized using Analog to Digital Converters (ADC's).
Each event is designated a channel number (based on the fluorescence intensity as originally detected by the PMT's) on a 1 - Parameter Histogram or 2 - Parameter Histogram.
All events are individually correlated for all the parameters collected.
Flow cytometric data is stored in FCS format, developed by the Society for Analytical Cytology.
Data Analysis

## Slide 30: 3. Electronics
Photomultiplier Tube (PMT) → PMTs convert light into electrical signals
The photodiode detectors or photo- multipler tubes first collect the light signal from the cells. The photons produce a pulse of electrical current.
Photomultiplier tubes have a voltage applied across a series of plates.
This increases their sensitivity so that fewer photons are required to produce an electrical current.
The initial small current requires amplification. The amplified current ranges from 0 to 10 V depending on the strength of the signal.
Data Analysis

## Slide 31
Data Analysis
A cell passes the laser interogation point and a signal is recorded…
Voltage Pulse of one cell:
Characteristics of the voltage pulse.

## Slide 32: How the voltage pulse signals are stored
Data Analysis
From every cell the maximum height (H) value every` signal, as well as the width (W) of the signal, as well as the area (A) of the signal is stored along with the time parameter.

## Slide 33: How histograms are created
Data Analysis

## Slide 34
1. Emission
2. Detection
3. Converted to voltages
4. Measured
5. File generated
6. Plotted
Summary

## Slide 35
Once a data file has been saved, cell population can be displayed as:
Dot plots:
1-Parameter Dot Plots vs. 2-Parameter Dot Plots
  Limitations: No density information (how many cells in a given range)
Data Analysis

## Slide 36
Data Analysis
Fluorescence one color histogram:
in conjunction with fluorescence-based protein reporters (GFP)
-> monitor both transfection efficiency and protein expression levels.

## Slide 37
Data Analysis
Density plots:
Provides the density of events in a given region
Three common ways to plot
Density
Zebra
Pseudocolor

## Slide 38: Contour Plots
Data Analysis
Each contour contains progressively less data
    First contour typically top 95% of data
Can mask actual amount of data
Don’t show outliers well / Use contour plot with outliers

## Slide 39
Data Analysis
Data generated in flow cytometry is displayed using Multiparameter Acquisition and Display software platforms.
Histograms corresponding to each of the parameters of interest can be analyzed using statistical tools to calculate percentage of cells manifesting specific fluorescence, and fluorescence intensity.
This information can be used to look at fluorescence expression within subpopulations of cells in a sample (GATING).
REGIONS and GATING …

## Slide 40
Data Analysis/Gating and Statistics
REGIONS
A region is a numerical or graphical boundary that is used to define the characteristics of particles to include for further analysis.
Drawing regions is often subjective, unless proper controls are used!
    Critical Controls:
      FMO control
      Biological Controls
        Stimulated samples
        Reference controls
Type of regions and how to place them:
Rectangular, Circles/ellipses, Polygon, Quadrants

## Slide 41: Types of Regions and how to place them
Data Analysis
Data generated in flow cytometry is displayed using Multiparameter Acquisition and Display software platforms.
Histograms corresponding to each of the parameters of interest can be analyzed using statistical tools to calculate percentage of cells manifesting specific fluorescence, and fluorescence intensity.
This information can be used to look at fluorescence expression within subpopulations of cells in a sample (GATING).
REGIONS and GATING …

## Slide 42
What gating means?
Gating uses regions to allow subsets of data to pass through to a downstream plot.
Gating is a data reduction method. Gate carefully!
Gating example: Doublet exclusion
Data Analysis/Gating and Statistics